IGN200, november 2013

NIT

Skills Exam, CCNP Route

- Time: 2 hours, including 30 minutes of design
- Full connectivity is required
- Every character of “show ip route” and
  “show ip bgp” must match on your routers
- TIP:
- R4# ping 172.16.1.1 source loopback 0
- R1# trace 192.168.4.4 source loopback 0
- You might use this command:
  neighbor X.Y.Z.W default-originate
- R4# ping 2001:1::1 source loopback 6

R1#show ip route

Gateway of last resort is 172.16.12.2 to network 0.0.0.0
R1

O*IA 0.0.0.0/0 [110/2] via 172.16.12.2, 00:16:04, GigabitEthernet0/0
      172.16.0.0/16 is variably subnetted, 6 subnets, 3 masks
C 172.16.1.0/25 is directly connected, Loopback0
L 172.16.1.1/32 is directly connected, Loopback0
C 172.16.1.128/25 is directly connected, Loopback1
L 172.16.1.129/32 is directly connected, Loopback1
C 172.16.12.0/24 is directly connected, GigabitEthernet0/0
L 172.16.12.1/32 is directly connected, GigabitEthernet0/0
R1#
R2# show ip route

Gateway of last resort is not set

     172.16.0.0/16 is variably subnetted, 8 subnets, 3 masks
O N2 172.16.1.128/25 [110/20] via 172.16.12.1, 00:16:46, FastEthernet0/0
C 172.16.23.0/24 is directly connected, FastEthernet0/1
R2
C 172.16.12.0/24 is directly connected, FastEthernet0/0
O 172.16.1.0/25 [110/2] via 172.16.12.1, 00:13:51, FastEthernet0/0
O 172.16.3.0/24 [110/2] via 172.16.23.3, 00:16:00, FastEthernet0/1
C 172.16.120.0/24 is directly connected, Loopback120
O 172.16.120.0/23 is a summary, 00:16:46, Null0
C 172.16.121.0/24 is directly connected, Loopback121
S 192.168.0.0/16 [1/0] via 172.16.23.3
R3# show ip route

Gateway of last resort is 192.168.43.4 to network 0.0.0.0

C 192.168.43.0/24 is directly connected, FastEthernet0/0
     172.16.0.0/16 is variably subnetted, 7 subnets, 4 masks
O E2 172.16.1.128/25 [110/20] via 172.16.23.2, 00:16:57, FastEthernet0/1
R3
C 172.16.23.0/24 is directly connected, FastEthernet0/1
O IA 172.16.12.0/24 [110/2] via 172.16.23.2, 00:16:57, FastEthernet0/1
S 172.16.0.0/16 is directly connected, Null0
O IA 172.16.1.0/25 [110/3] via 172.16.23.2, 00:14:48, FastEthernet0/1
C 172.16.3.0/24 is directly connected, Loopback0
O IA 172.16.120.0/23 [110/2] via 172.16.23.2, 00:16:57, FastEthernet0/1
C 192.168.34.0/24 is directly connected, Serial0/1/0
B* 0.0.0.0/0 [20/0] via 192.168.43.4, 00:09:13
R3#show ip bgp
  Network Next Hop Metric LocPrf Weight Path
* 0.0.0.0 192.168.34.4 0 30 0 65400 i
*> 192.168.43.4 0 40 0 65400 i
*> 172.16.0.0 0.0.0.0 0 32768 i
R4#show ip route

Gateway of last resort is not set

C 192.168.43.0/24 is directly connected, FastEthernet0/0
R4
B 172.16.0.0/16 [20/10] via 192.168.43.3, 00:09:58
C 192.168.4.0/24 is directly connected, Loopback0
C 192.168.34.0/24 is directly connected, Serial0/0/0
R4#show ip bgp
   Network Next Hop Metric LocPrf Weight Path
* 172.16.0.0 192.168.34.3 20 0 65100 i
*> 192.168.43.3 10 0 65100 i

R1#show ipv6 route
IPv6 Routing Table - default - 6 entries
Codes: C - Connected, L - Local, S - Static, U - Per-user Static route
       B - BGP, HA - Home Agent, MR - Mobile Router, R - RIP
       I1 - ISIS L1, I2 - ISIS L2, IA - ISIS interarea, IS - ISIS summary
       D - EIGRP, EX - EIGRP external, NM - NEMO, ND - Neighbor Discovery
       l - LISP
       O - OSPF Intra, OI - OSPF Inter, OE1 - OSPF ext 1, OE2 - OSPF ext 2
      ON1 - OSPF NSSA ext 1, ON2 - OSPF NSSA ext 2
R1

C 2001:1::/64 [0/0]
     via Loopback6, directly connected
L 2001:1::1/128 [0/0]
     via Loopback6, receive
R 2001:4::/64 [120/2]
     via FE80::C0A8:404, Tunnel0
C 2001:14::/64 [0/0]
     via Tunnel0, directly connected
L 2001:14::1/128 [0/0]
     via Tunnel0, receive
L FF00::/8 [0/0]
     via Null0, receive
R1#
R4#show ipv6 route
IPv6 Routing Table - Default - 6 entries
Codes: C - Connected, L - Local, S - Static, U - Per-user Static route
       B - BGP, HA - Home Agent, MR - Mobile Router, R - RIP
       I1 - ISIS L1, I2 - ISIS L2, IA - ISIS interarea, IS - ISIS summary
       D - EIGRP, EX - EIGRP external
       O - OSPF Intra, OI - OSPF Inter, OE1 - OSPF ext 1, OE2 - OSPF ext 2
       ON1 - OSPF NSSA ext 1, ON2 - OSPF NSSA ext 2

R 2001:1::/64 [120/2]
R4
     via FE80::AC10:101, Tunnel0
C 2001:4::/64 [0/0]
     via Loopback6, directly connected
L 2001:4::4/128 [0/0]
     via Loopback6, receive
C 2001:14::/64 [0/0]
     via Tunnel0, directly connected
L 2001:14::4/128 [0/0]
     via Tunnel0, receive
L FF00::/8 [0/0]
     via Null0, receive
R4#

R1#show running
Building configuration...

Current configuration : 2194 bytes
!
! Last configuration change at 07:26:56 UTC Fri Nov 1 2013
version 15.1
service timestamps debug datetime msec
service timestamps log datetime msec
no service password-encryption
!
hostname R1
!
ipv6 unicast-routing
ipv6 cef
ip source-route
ip cef
!
interface Loopback0
 ip address 172.16.1.1 255.255.255.128
 ip ospf network point-to-point
!
interface Loopback1
 ip address 172.16.1.129 255.255.255.128
!
interface Loopback6
 no ip address
 ipv6 address 2001:1::1/64
 ipv6 rip KALLE enable
!
interface Tunnel0
 no ip address
 ipv6 address 2001:14::1/64
 ipv6 rip KALLE enable
 tunnel source Loopback0
 tunnel mode ipv6ip
 tunnel destination 192.168.4.4
!
interface Embedded-Service-Engine0/0
 no ip address
 shutdown
!
interface GigabitEthernet0/0
 ip address 172.16.12.1 255.255.255.0
 duplex auto
 speed auto
!
interface GigabitEthernet0/1
 no ip address
 shutdown
 duplex auto
 speed auto
!
interface Serial0/1/0
 no ip address
 shutdown
 no fair-queue
!
interface Serial0/1/1
 no ip address
 shutdown
 clock rate 2000000
!
router ospf 1
 router-id 1.1.1.1
 area 25 nssa
 redistribute connected subnets
 network 172.16.1.0 0.0.0.127 area 25
 network 172.16.12.0 0.0.0.255 area 25
!
ip forward-protocol nd
!
no ip http server
no ip http secure-server
!
ipv6 router rip KALLE
!
control-plane
!
mgcp profile default
!
gatekeeper
 shutdown
!
line con 0
line aux 0
line 2
 no activation-character
 no exec
 transport preferred none
 transport input all
 transport output lat pad telnet rlogin lapb-ta mop udptn v120 ssh
 stopbits 1
line vty 0 4
 login
 transport input all
!
scheduler allocate 20000 1000
end

R1#
R2#show running
Building configuration...

Current configuration : 1460 bytes
!
version 12.4
service timestamps debug datetime msec
service timestamps log datetime msec
no service password-encryption
!
hostname R2
!
boot-start-marker
boot-end-marker
!
logging message-counter syslog
!
no aaa new-model
memory-size iomem 5
dot11 syslog
ip source-route
!
!
!
!
ip cef
no ipv6 cef
!
multilink bundle-name authenticated
!
voice-card 0
!
vtp domain cisco.com
vtp mode transparent
archive
 log config
  hidekeys
!
interface Loopback120
 ip address 172.16.120.1 255.255.255.0
!
interface Loopback121
 ip address 172.16.121.1 255.255.255.0
!
interface FastEthernet0/0
 ip address 172.16.12.2 255.255.255.0
 duplex auto
 speed auto
!
interface FastEthernet0/1
 ip address 172.16.23.2 255.255.255.0
 duplex auto
 speed auto
!
interface Serial0/1/0
 no ip address
 shutdown
 no fair-queue
 clock rate 2000000
!
interface Serial0/1/1
 no ip address
 shutdown
 clock rate 2000000
!
router ospf 1
 router-id 2.2.2.2
 log-adjacency-changes
 area 25 nssa no-summary
 area 53 range 172.16.120.0 255.255.254.0
 network 172.16.12.0 0.0.0.255 area 25
 network 172.16.120.0 0.0.1.255 area 53
 network 172.16.0.0 0.0.255.255 area 0
!
ip forward-protocol nd
ip route 192.168.0.0 255.255.0.0 172.16.23.3
no ip http server
no ip http secure-server
!
control-plane
!
mgcp fax t38 ecm
!
line con 0
line aux 0
line vty 0 4
 login
!
scheduler allocate 20000 1000
end

R2#

R3#show running
Building configuration...

Current configuration : 1976 bytes
!
version 12.4
service timestamps debug datetime msec
service timestamps log datetime msec
no service password-encryption
!
hostname R3
!
boot-start-marker
boot-end-marker
!
no aaa new-model
memory-size iomem 15
dot11 syslog
ip source-route
!
ip cef
no ip domain lookup
no ipv6 cef
!
multilink bundle-name authenticated
!
vtp domain cisco.com
vtp mode transparent
archive
 log config
  hidekeys
!
interface Loopback0
 ip address 172.16.3.3 255.255.255.0
 ip ospf network point-to-point
!
interface FastEthernet0/0
 ip address 192.168.43.3 255.255.255.0
 duplex auto
 speed auto
!
interface FastEthernet0/1
 ip address 172.16.23.3 255.255.255.0
 duplex auto
 speed auto
!
interface Serial0/1/0
 ip address 192.168.34.3 255.255.255.0
 no fair-queue
!
interface Serial0/1/1
 no ip address
 shutdown
 clock rate 2000000
!
interface Serial0/2/0
 no ip address
 shutdown
 clock rate 2000000
!
interface Serial0/2/1
 no ip address
 shutdown
 clock rate 2000000
!
router ospf 1
 router-id 3.3.3.3
 log-adjacency-changes
 network 172.16.0.0 0.0.255.255 area 0
!
router bgp 65100
 no synchronization
 bgp log-neighbor-changes
 network 172.16.0.0
 neighbor 192.168.34.4 remote-as 65400
 neighbor 192.168.34.4 route-map LOCAL30 in
 neighbor 192.168.34.4 route-map MED20 out
 neighbor 192.168.43.4 remote-as 65400
 neighbor 192.168.43.4 route-map LOCAL40 in
 neighbor 192.168.43.4 route-map MED10 out
 no auto-summary
!
ip forward-protocol nd
ip route 172.16.0.0 255.255.0.0 Null0
no ip http server
no ip http secure-server
!
route-map LOCAL40 permit 10
 set local-preference 40
!
route-map MED10 permit 10
 set metric 10
!
route-map MED20 permit 10
 set metric 20
!
route-map LOCAL30 permit 10
 set local-preference 30
!
end
R4#show running
Building configuration...

Current configuration : 1648 bytes
!
version 12.4
service timestamps debug datetime msec
service timestamps log datetime msec
no service password-encryption
!
hostname R4
!
boot-start-marker
boot-end-marker
!
logging message-counter syslog
!
no aaa new-model
memory-size iomem 5
!
dot11 syslog
ip source-route
!
ip cef
!
no ip domain lookup
ipv6 unicast-routing
ipv6 cef
!
multilink bundle-name authenticated
!
voice-card 0
!
vtp domain cisco.com
vtp mode transparent
archive
 log config
  hidekeys
!
interface Loopback0
 ip address 192.168.4.4 255.255.255.0
!
interface Loopback6
 no ip address
 ipv6 address 2001:4::4/64
 ipv6 rip KALLE enable
!
interface Tunnel0
 no ip address
 ipv6 address 2001:14::4/64
 ipv6 rip KALLE enable
 tunnel source Loopback0
 tunnel destination 172.16.1.1
 tunnel mode ipv6ip
!
interface FastEthernet0/0
 ip address 192.168.43.4 255.255.255.0
 duplex auto
 speed auto
!
interface FastEthernet0/1
 no ip address
 shutdown
 duplex auto
 speed auto
!
interface Serial0/0/0
 ip address 192.168.34.4 255.255.255.0
 no fair-queue
 clock rate 2000000
!
interface Serial0/0/1
 no ip address
 shutdown
 clock rate 2000000
!
router bgp 65400
 no synchronization
 bgp log-neighbor-changes
 neighbor 192.168.34.3 remote-as 65100
 neighbor 192.168.34.3 default-originate
 neighbor 192.168.43.3 remote-as 65100
 neighbor 192.168.43.3 default-originate
 no auto-summary
!
ip forward-protocol nd
no ip http server
no ip http secure-server
!
ipv6 router rip KALLE
!
control-plane
!
line con 0
line aux 0
line vty 0 4
 login
!
scheduler allocate 20000 1000
end